## Slide 1
4-Quadrant VFD Hoist Drive

## Slide 2
CONTENTS
01
Active Load Challenge
02
Power Stage Topology
03
Dynamic Braking Guard
04
Scalar Control Scheme
05
Time-Domain Results

## Slide 3
CONTENTS
06
Four-Quadrant Map
07
Conclusions

## Slide 4
Active Load Challenge
01

## Slide 5
Gravity-Driven Load Dynamics
A hoist presents a unique control challenge: it is an active load governed by gravity, demanding bidirectional power flow.
Lifting (Motoring)
The motor works against gravity, converting electrical energy to potential energy.
Lowering (Regeneration)
Gravity pulls the load; the motor must brake to control descent, acting as a generator.

## Slide 6
Power Stage Topology
02

## Slide 7
The Simulink Diagram

## Slide 8
AC-DC-AC Conversion Chain
Grid
500V, 50Hz
Stiff Source
Rectifier
Uncontrolled
Diode Bridge
DC Link
2200 µF
Capacitor
Inverter
2-Level
IGBT Bridge
Motor
4kW
Induction Motor

## Slide 9
Dynamic Braking Guard
03

## Slide 10
Braking Chopper Protection
The unidirectional diode rectifier cannot return energy to the grid. During lowering, the motor acts as a generator, which would cause a dangerous rise in DC bus voltage.
The Solution: Dynamic Braking
A hysteresis-controlled IGBT chopper and resistor bank act as a safety valve, dissipating excess regenerative energy to protect the DC link components.
Rising VDC
Hysteresis Control
If VDC > 700V: IGBT ON
If VDC < 650V: IGBT OFF
Energy Dissipated in 60 Ω Resistor

## Slide 11
Scalar Control Scheme
04

## Slide 12
V/f Control with SPWM Modulation
Scalar V/f Control
An open-loop strategy to maintain constant air-gap flux by keeping the ratio of stator voltage to frequency constant.
( \frac{V}{f} \approx \text{Constant} )
Sinusoidal PWM (SPWM)
A high-frequency (1 kHz) triangular carrier wave is compared with a low-frequency sine wave reference to generate gating pulses for the IGBTs.
Reference Sine
(Desired Freq.)
Triangular Carrier
(1 kHz)
SPWM Pulses

## Slide 13
Time-Domain Results
05

## Slide 14
Speed & Torque Response
Rotor Speed
The motor accelerates to +10 rad/sec, decelerating to a stop, and then reversing to -10 rad/sec.
Electromagnetic Torque

## Slide 15
DC Bus Voltage Clamping
During regeneration, the DC bus voltage is actively clamped by the braking chopper, preventing catastrophic over-voltage.
650 V
Lower Limit
(Chopper OFF)
700 V
Upper Limit
(Chopper ON)

## Slide 16
Four-Quadrant Map
06

## Slide 17
Torque-Speed Quadrant Loop
The XY plot of Torque (Y) vs. Speed (X) provides a clear visualization of the machine's four-quadrant operation.
Quadrant I (Forward Motoring)
+Speed, +Torque. Power is positive. Energy flows from grid to motor.
Quadrant II (Reverse Regeneration)
-Speed, +Torque. Power is negative. Energy flows from load to DC bus, confirming regeneration.

## Slide 18
Conclusions
07

## Slide 19
Validated Drive Performance
Stable Torque Control
The drive successfully maintains positive torque against gravity in both motoring and regenerative modes.
Effective Protection
The dynamic braking chopper successfully clamped the DC bus voltage, preventing component damage.
Industrial Suitability
The VFD topology is proven suitable for safe and reliable operation in industrial hoist and crane applications.

## Slide 20
THANK YOU